## Slide 1: AVL Hardware
Onboard the Train:
  GPS (Global Positioning System) Unit
    Reports location of train in realtime
    Communicates with onboard Master PC
Image source: Numerex

## Slide 2: APC Hardware
Onboard the Train:
  Bi Directional Infrared Sensor Bars
    Accurately records occupancy by tracking incoming and outgoing passengers
    Communicates with onboard Master PC
Image source: INIT systems

## Slide 3: Onboard Master PC
Underlying Hardware:
  ARM SBC
  Runs Linux (free!)
  Easily Adaptable
  802.11 / GPRS Capable
Designed to receive input from many onboard AVL units and APC units
  Serial RS-232 & RS-485
  Long range RF
  USB
Image sources: Technologic Systems

## Slide 4: Server Architecture
X86 based Intel processors
Database server
  Large disk size
  Redundancy & Backups
Optimization & Decision server
Web App Server(s)
  Clustered & Load Balanced w/ HA

## Slide 5: Physical Servers vs. Virtual Servers
Virtualization allows for longevity and ease of maintenance versus a physical server.
However, transit organizations may want to have a physical box on site for local management.
This flexibility allows for solutions at multiple price points.
  Local physical servers
  Local virtual servers
  Remote servers